## Slide 1: S.M.A.R.T Claw Team T7

## Slide 2
Project Introduction
Introduction
01

## Slide 3
Christian Lee
Lead Designer
Meet the T7 Team
Tony Tang
Claw Manufacturing Lead
Om Chaudhari
CAD & Drawings Lead
Shaiv Ramdhani
Programming Lead
Rohin Dhaliwal
Prototypes & Experiments Lead
Notes: christian

## Slide 4
Design Challenge
Our goal is to design a fully autonomous retrieval system. The design should serve as a small-scale prototype of a device to be used in retrieving the UFO from the Pacific Ocean.

## Slide 5
Design Specifications
Requirements | 
R1 | Device must use NO MORE THAN ONE of each of (1) Arduino board, (2) servo motor, and (3) ultrasonic sonar
R2 | Device must be able to pick up and release an object autonomously; only raising and lowering can be controlled by a human operator
R3 | The device must only be constructed from materials listed in Table 1 of the Module 5 rules document
R4 | The device must be able to deposit objects into a 8ft x 8ft box with a height of 2in
Evaluation Criteria | 
C1 | The greater the number of Round 1 objects that the device can retrieve, the better
C2 | The greater the number of 1.25in cubes the claw device can simultaneously retrieve, the better
C3 | The smaller the delay between detecting the object and retrieving / releasing it, the better
C4 | The lesser the degree of unwanted swinging or rotating when attached to the crane, the better
C5 | The lower the number of moving parts (and hence the lower the risk of mechanical failure), the better
A list of requirements and evaluation criteria influenced by the competition rules
Notes: Rohin

## Slide 6: Risk Management Code Optimization Extensive Prototyping
Use risk identification and registers throughout our project
Minimize risks through experiments
Prototype as many feasible designs as possible
Experiment and prototype using rapid construction materials
Approach code design with the same degree of rigour as the retrieval device
Code should minimize wasted time and accurately retrieve objects
Design Strategy
Notes: Chris and Rohin

## Slide 7
Project Introduction
Concept Generation
02

## Slide 8
Initial C-Sketches
Half Octopus - C.L.
The Crab - R.D.
Engulfer - S.R.
The Trapper - O.C.
Scooper - T.T.
Notes: Rohin

## Slide 9
Individual Sketches
The CAGE claw - C.L.
The Trapper - S.R
The Tightener - R.D.
The Excavator - O.C
Three-Way Split- T.T
Notes: Rohin

## Slide 10
Prototypes & Concept Evaluation
Prototypes & Concept
Evaluation
03

## Slide 11
First Prototype – “Trapper” Concept
Strengths: easy to build; strings provide enough force to lift a pencil case
Weaknesses: limited range of motion; claw relies solely on friction to lift objects
Notes: Rohin

## Slide 12
Second Prototype – Adding Angled Tips
Strengths:
Can pick up heavy objects (e.g. stapler)
Replacement of string with rigid wire increased range of motion of claw (wires can both pull and push the claw arms)
Weaknesses:
Round objects may slide out of the sides of the claw arms
Cardboard connected with hot glue is structurally weak
Angled Tips
Notes: Rohin

## Slide 13
Prototyping Hinge Mechanisms
Tape Hinge
Strengths:
Easy to construct
Quickly Adjustable
Weaknesses:
Lower strength (but enough to hold Round 1 & 2 objects)
Slightly flimsy
Rank - 1 (Chosen Design)
Side Hinge
Strengths:
Smooth rotation
Full range of motion
Weaknesses:
Construction time is lengthy
Difficult to align claw arms precisely
Rank - 2
Three Section Hinge
Strengths:
Highest durability
Precise alignment of arms
Weaknesses:
Assembly of panels is difficult
Additional friction increases force required by servo motor
Rank - 3
Notes: Shaiv

## Slide 14
Testing Use of Rubber Lining
With Rubber
Strengths:
Stronger grip on objects
Less force required from servo
Weaknesses:
Can disrupt alignment of claw arms
Can get caught on the ground
Without Rubber
Strengths:
Can scoop objects by smoothly sliding against the ground
Weaknesses:
Cannot hold heavier objects with low coefficients of friction
More force needed from servo
Conclusion: Ideal for Round 1
Increased friction improves chances of retrieving a wide variety of objects
Conclusion: Ideal for Round 2
Aluminum edges can scoop along the floor and retrieve multiple objects
Notes: Shaiv

## Slide 15
Testing Round 2 Specialized Claw
Test Notes:
We tested a larger claw arm tailored for bulk objects Round 2
The imprecise cuts in the metal prevent an equal force distribution, causing a few cubes to slip out of the claw arm
Our solution was using popsicle sticks to extend the claw
Larger Claw Arm Attachments
Notes: Shaiv

## Slide 16
Prototypes & Concept Evaluation
Risks, Experiments
& Concept Selection
04

## Slide 17
Risk Register |  |  | 
Risk | Classification | Rating | Risk Management Strategy
Servo motor does not produce enough force to pick up objects. | Technical Preventable | 6 | Design an experiment to test the ideal placement and attachment of wiring in order to maximize the force
Sonar sensor has issues and interrupts the flow of our code. | Technical Strategic | 12 | Implement debouncing mechanism in code to counter variance Trial sonars to find best functioning one Backup code functioning off a timer
Any mechanical or technical failure on the day of the competition. | Project Management Preventable | 5 | Find functioning components and fully charge batteries Don’t excessively test our components
Scarcity of aluminium may require the use of weaker cardboard. Cardboard components are flimsy impacting our claws performance. | Technical Strategic | 4 | Test to see high stress areas in our claw High stress areas can be made of aluminium Lower stress area can be made of cardboard
Rubber tubing attachments drag on floor and prevent full closure. | Technical Strategic | 8 | Test between having the tubing and not having it Use two attachments that can be swapped out depending on object

## Slide 18
Risk Experiment 1: Wire Attachment Optimization
Research Question #1: What is the optimal positioning for the wires connecting the claw arms and the servo?
Research Question #2: How can we maximize the force without comprising the width of the claw?
Lower Wire Attachment
More force translated through claw
Smaller width of claw
Risk that jaw opening may not be wide enough to grab objects
Higher Wire Attachment
Less force translated through claw
Risk of lowering output force when retrieving objects
Larger claw width

## Slide 19
Risk Experiment 1: Wire Attachment Optimization
Experimental Setup & Procedure
Tested attaching the wires at distances 1-10 cm from the top of the claw
Measured the maximum amount of water in a water bottle held for each increment.
Measured the widest gap in between the two claw arms
Graphed scaled results
Volume of Water Lifted and Maximum Claw Width as Functions of Wire Position
Conclusion:
A wire position of 8 cm from the top yielded ideal results to mitigate risk.

## Slide 20
Risk Experiment 2: Sonar Reliability
Key Findings
Readings were compared to a ruler
0 cm was consistently accurate
Between 1 and 5 cm did not register anything
Peak accuracy between roughly 17-25 cm from the ground
This means our sonar should be set to trigger within this optimal range to avoid sonar malfunctions
Sonar Accuracy as a Function of Distance from Ground
Research Question: At what distance from the ground is the sonar most reliable?

## Slide 21
Weighted Decision Matrix
All 5 concepts passed screening
We elected to skip ranking due to a low number of concepts
We built our criteria based on our evaluation criteria and integrated Experiment 1 & 2 results in our evaluation
We distributed the criteria weights based on competition rules and team strategy

## Slide 22
Weighted Decision Matrix
Final WDM resulted in The Excavator being the most promising concept.
Sensitivity analysis to ensure robustness:
  Excavator remained our top concept
  Minor changes across lower scoring concepts
  Indicates our results are valid

## Slide 23
Final Design
05

## Slide 24
Final Design: The S.M.A.R.T Claw

## Slide 25: Modular Attachment 1 Modular Attachment 2 Pins
For Round 1 (Variety Objects)
Applies a focused force across a 4in span
Useful for heavier objects such as the can
For Round 2 (bulk objects)
Distributes force across 8in length for lifting multiple objects
Cubes are lightweight so we can pick up roughly 16 at once (8 x 2 grid)
Pins are made from red tubing and black rod
Pin system creates secure connections
Notes: Rohin

## Slide 26
Rubber Lined Edges
Insertable red rubber lining on the edges of the claw, enhancing grip, handling, and friction between claw and object
Tape Hinges
Loosely attaches claw arms, minimizing the force required to open and close the arms while still providing a secure connection
Copper Wire Mechanism
The use of rigid wires efficiently generates force to open the claws wide, and sufficient force to firmly grab any Round 1 or 2 object without slipping
Final Design Features
Rubber Lined Edges

## Slide 27
Final Design Dimensions
Analysis:
The 6x4 in2 dimensions of the base ensure that the widest object in the competition can be fully enclosed inside of the boxed claw
The 4x5.3 in2 dimensions of the claw ensure that the tallest object in the competition can be fully enclosed inside the claw
The claw edges make a 14° angle to the claw arm, which is suitable to retrieve an object while minimizing friction with the ground

## Slide 28
Final Design Code Flowchart
Start
Close Claw
Distance < PICKUP_DIST for DEBOUNCE ?
Open Claw
Close Claw
Wait DELAY_TIME
Wait OPEN_TIME
Symbolic Constants:
PICKUP_DISTANCE = 25cm
OPEN_TIME = 3000ms
DELAY_TIME = 2000ms
DEBOUNCE = 500ms
Notes: Rohin

## Slide 29
Project Introduction
Reflection
06

## Slide 30: Round 1 Reflection Code functioned as intended   Sonar risk experiment results eliminated any sonar malfunctions Challenges emerged in positioning of objects Improvements Develop a claw where spinning about the vertical axis is not as problematic Improve claw width   In our risk experiment 1, we prioritized force over claw width   This decision may have been misguided as smaller claw width required more accuracy to pick up objects Round 2 Reflection Modular attachments enhanced pickup capability and overall performance   Enabled claw to pick up many cubes at once Prototyped rubber lining maximized grip and reduced the force required per cube Improvements Uneven force distribution across claw arms caused cube instability when transporting to drop off zone
Competition Reflection

## Slide 31: Om Chaudhari: Project Introduction & Risks Rohin Dhaliwal: Prototypes & Concept Selection Christian Lee: Concept Generation & Final Design Shaiv Ramdhani: Experiments & Final Design Tony Tang: Reflection Team T7 did not utilize Generative AI in this project
Contributions